## Slide 1: USING HAM RADIO
How to make your first contact
This presentation was provided by the San Joaquin County Emergency Medical Services Agency
for the members of the San Joaquin Operational Area Healthcare Coalition.
Funding was provided by the 2012/13 Hospital Preparedness Program (HPP) Grant.

## Slide 2: What you’ll learn
Repeaters and Simplex
Making your first contact
That a little ham-speak is all you need
4. How to select a channel
5. Who to talk to
6. Following FCC rules
San Joaquin County Emergency Medical Services Agency

## Slide 3: Repeaters and simplex
Simplex:
Single frequency
Limited to line-of-site
Handie-talkie range <2 miles
Mobile range maybe 12 miles
Hospital range
20-25 miles
Repeaters:
Use two frequencies at the same time – input and output
Are located at tall places
Extend the range of portables/mobiles
We use repeaters for communication
San Joaquin County Emergency Medical Services Agency
Notes: Your Technician Class Amateur Radio License allows you to communicate using both simplex and repeaters – and well as do other things we won’t talk about here. Simplex means you transmit and receive on a single frequency. Using simplex, all the radios are talking to one another directly. Because of distance limitations some stations may not hear each other. On the frequencies we use in the 2-meter and 70-centimeter – that is 144 MHz. VHF and 440 MHz UHF – signals travel line-of-sight. This limits range for portables talking to portables to a few miles or less. Mobiles talking to other mobiles will talk father, up to a dozen miles or so. Base stations with tall antennas can communication with one another over dozens of miles.
Repeaters were created to overcome the line-of-sight limitation. Repeaters are two-frequency radio systems usually placed at high locations on towers, buildings or hills. Because they are hundreds to thousands of feet above the users, the repeater’s line-of-sight can extend to 100 miles or more. All stations that can “see” the repeater can communicate through it, although portable range will be much smaller than the distance from which a mobile station can communicate through a repeater.
Repeaters are two frequency systems. The repeater listens on one frequency – called the input frequency – and transmits on another frequency – called the output. What the repeater “hears” on the input frequency is simultaneously retransmitted on the output frequency. Your radio transmits on the input frequency and listens on the output frequency. It hears other stations that are retransmitted by the repeater. It does not hear other stations directly, as on simplex.

## Slide 4: Using repeaters
Most local communication uses repeaters to improve coverage
Portables will not always be able to specific repeaters, but should always hit one or more repeaters in SJC
Repeaters are known by their frequency and/or location
Repeaters often require a PL tone to operate
We offer free radio programming to solve these challenges
San Joaquin County Emergency Medical Services Agency
Notes: Most local communication uses repeaters to improve coverage. Because of their low power – typically five watts or less – portable radios will be able to talk though – or hit – repeaters at fairly close distances. Mobile radios, typically running 50 watts, can communicate through repeaters from much larger distances. Remember that anyone who can hit the repeater can talk to anyone else who can hit the repeater. That means people who could never communicate directly can communicate through a repeater.
Repeaters are typically known by their output frequencies, locations or both.
In order to avoid interference from other repeater users, most repeaters require a subaudible tone to be transmitted in order to trigger the repeater. This tone – usually referred to as a PL Tone or Tone Squelch – must be transmitted to operate the repeater. The PL tone can be set manually or programmed into a radio’s memory channels, along with the required split, offset and even an alphanumeric channel name.

## Slide 5: Your first contact
What to do:
Select a repeater that is close to you.
Listen to make sure you will not be interfering with others
Press the push-to-talk switch on the radio or microphone
Wait 2 seconds before speaking
What to say:
With your mouth two inches from the microphone, announce your call sign and say “listening”
Release the push-to-talk switch
San Joaquin County Emergency Medical Services Agency
Notes: Many new Amateurs are frightened of using repeaters. They should not be. Repeaters are easy to use and communities of hams congregate around many repeaters, especially those affiliated with Amateur Radio clubs.
If your radio is programmed for a nearby repeater, making a contact is easy.
First, listen to make sure no one is using the repeater. When it is available, press the push-to-talk switch and announce your callsign, followed by the word “listening.” If all goes well – meaning your radio is programmed correctly – you will hear something back from the repeater. Typically you will hear the repeater carrier – a quiet signal – and perhaps what is called a courtesy tone. If the repeater has not been used for a few minutes it may also identify itself using voice or Morse code.
If someone is listening to the repeater, they may answer you, perhaps giving your callsign followed by their callsign. Or they may give their callsign only. The other operator may offer a greeting. When the other station stops transmitting, you should hear the courtesy tone (if there was one) again. That is your cue to resume speaking.
In the future, if you wish to contact any station, just announce your callsign and say listening. If you want a specific station, give their callsign first, followed by your callsign. “N6TEC this is N5FDL calling” or words to that effect. If you wish to join a conversation in progress, just announce your callsign. If you need to interrupt or make an emergency call, use the words “BREAK BREAK” to signify that you have an emergency.

## Slide 6: What do hams talk about?
Pretty much anything, but radio is popular, along with club events, family talk between hams.
Hams talk about most subjects.
Broadcasting, music and singing is illegal.
So is swearing.
San Joaquin County Emergency Medical Services Agency

## Slide 7: Ending a conversation
When finished, give your callsign followed by “clear.”
To call another station, just announce their callsign first followed by your own.
“N6TCY, this is N5FDL calling” or something similar.
San Joaquin County Emergency Medical Services Agency

## Slide 8: Id’s and callsigns
The FCC requires your callsign be given every 10 minutes and at the end of communication.
Tactical callsigns are sometimes used in addition to personal callsigns. Tactical callsigns are unofficial, used to make it easier to contact specific locations or functions.
Each facility has a tactical callsign (usually the facility name) and every operator has an FCC-assigned personal callsign.
During an exercise or emergency, tactical calls will be used. You must still ID with your own callsign as required by the FCC.
San Joaquin County Emergency Medical Services Agency

## Slide 9: Where to learn more
There are many excellent books about Amateur Radio. The best place to find them is on the ARRL website (arrl.org). QST is the monthly magazine of Amateur Radio. ARRL is the national organization for Amateur Radio.
There are four Amateur Radio Clubs in San Joaquin County and all welcome visitors and new members. Details at n5fdl.com.
Get on-the-air and ask questions! The SJC2 Channel 22 repeater in Tracy is a good place to start. Likewise SJC4 Channel 24 in Lodi.
Send email or call with questions, to get HamCram information or arrange for free radio programming – david@coursey.com.
San Joaquin County Emergency Medical Services Agency